## Slide 1
SUBNET MASK
A subnet mask allows users to identify which part of an IP address is reserved for the network and which part is available for host use.
Adding the subnet mask or netmask gives users all the information needed to calculate network and host portions of the address with ease.
It can allow users to easily calculate whether IP addresses are on the same subnet or not.

## Slide 2
DEFAULT IP ADDRESS
When applying the two rules of subnetting to classful addresses, the default subnet mask for different classes of the ip addresses are:
Class A = 255.0.0.0
Class B = 255.255.0.0
Class C = 255.255.255.0
Where 255 represents network prefix and 0 represents host suffix. In the above table 255.0.0.0 is a standard class A subnet mask, since the first bit are all once (network) and the last three bites are all zeros (host). When this subnet mask is applied to a class A network, no subnetting is performed.
zzzz

## Slide 3
DETERMINING THE NETWORK PORTION OF THE HOST ADDRESS AND
ROLE OF SUBNETMASK
To determine what the network address is for any given IP address, users merely have to convert both octal addresses into binary and do a bitwise AND operation.
Here is an example of using an IP address of 156.154.81.56 with a network mask of 255.255.255.240
IP Address: 10011100.10011010.01010001.00111000
Subnet mask: 11111111.11111111.11111111.11110000
Bitwise AND : ———————————————–
Result: 10011100.10011010.01010001.00110000

## Slide 4
ANDing PROCESS
When a source host attempts to communicate with a destination host, the source host uses its subnet mask to determine whether the destination host is on the local network or a remote network.
This is known as the ANDing process.
The AND function has the following properties:
If the two compared values are both 1, the result is 1.
If one of the values is 0 and the other is 1, the result is 0.
If both of the compared values are 0, the result is 0.

## Slide 5
For example two hosts that want to communicate. Host A (with IP address 172.16.2.4) wants to communicate with Host B (with IP address 172.16.3.5). The subnet mask for Host A is 255.255.0.0
Using the ANDing process:
When converted to binary, the address 172.16.2.4 is:
10101100 00010000 00000010 00000100
When converted to binary, the address 172.16.3.5 is:
10101100 00010000 00000011 00000101
If the ANDing process is performed,
The result for Host A using its subnet mask of 255.255.0.0 is
HOST A's IP Address 10101100 00010000 00000010 00000100
Host A's Subnet Mask 11111111 11111111 00000000 00000000
ANDING Result 10101100 00010000 00000000 00000000
The result for Host B is
HOST B's IP Address 10101100 00010000 00000011 00000101
Host A's Subnet Mask 11111111 11111111 00000000 00000000
ANDing Result 10101100 00010000 00000000 00000000